## Slide 1: Crumbles® Technology
forestconcepts
International Biomass Conference April 22,2015
Reactor-ready Feedstocks The next generation of supply chain technologies

## Slide 2: What is this Crumbles® Stuff?
Flows like grain
Crumble at Field Moisture
Don’t dry unless needed
Dry After milling when needed
OBTW – 1/3 the energy of hammer milling

## Slide 3: Who is Forest Concepts?
Formed in 1998
Eight full-time regular employees
Based in Auburn, WA
A technology developer at the intersection of biology, engineering, and enterprise
  Bioenergy – Crumbles®, Beneficiation, and Baling
  Environmental Restoration – ELWd™ and WoodStraw®
  Distributed-scale enterprises
28 Issued US Patents in 4 technology families
  Biomass balers, Crumbles®, WoodStraw®, Beneficiation

## Slide 4: Erosion Control How would Nature do it?

## Slide 5: WoodStraw® 1.0

## Slide 6: WoodStraw® 2.0

## Slide 7: Cellulosic Biofuel Feedstocks 2008 Worldview
Corn stover and switchgrass are EASY!
Woody feedstocks are a pain in the butt!
  Too much energy to make
  Too much energy to dry
  Don’t flow for beans
  Chips are not the right format

## Slide 8: Sound Science – Disciplined Engineering
How does length, width and thickness matter?
What dimensions need to be controlled?
How does conversion process matter?
What are system-optimal particle properties?
What is the theoretical minimum comminution energy to convert logs into ideal feedstock particles?
(about 75-100 MJ/Mg for 2mm GMD)

## Slide 9: Wood Pathways
Crushing and Scrimming
Veneer and Crumbling
Chipping and Crumbling
Grinding and hammer-milling

## Slide 10: Plants are Different!
Radial
Longitudinal
Tangential
Fiber Direction

## Slide 11: Wood Pathways
Crushing and Scrimming
Veneer and Crumbling
Chipping and Crumbling
Grinding and hammer-milling

## Slide 12: Crumbles® from Veneer
Industrial veneer from logs
High transport density
Controls thickness dimension
Enables separation of heartwood, sapwood and bark
Enables orientation with grain for next processing operation

## Slide 13: Video
Crumbler M24 overview

## Slide 14: Crumbles® Particles
Precision particles
Physical properties are optimizable for specific conversion processes
  Length
  Thickness
  Moisture
  Uniformity of size
  Flowability
Two pathways
  From veneer
  From chips
Cascading processing of chip - particle size converges on cutter thickness
  Minimal production of fines

## Slide 15: 1.6mm Crumbles® From Chips Size Distribution and Energy
Poplar chips Summary | Process | Output GMD | Moisture | Mass | Total E | Specific E
Sample ID | Size (mm) | (Xgm, mm) | (%wb) | (odkg) | (MJ/odMg) | (MJ/odMg)
2013.10.10.001.01 | Raw Chips | 11.82 | 55.0% |  |  | 
2013.10.10.001.01.A | 4.79 | 5.39 | 54.4% | 14.73 | 36.2 | 19.5
2013.10.10.001.01.A.A | 1.59 | 2.63 | 54.6% | 13.56 | 94.2 | 58.5
2013.10.10.001.01.A.A.A | 1.59 | 1.97 | 54.6% | 12.56 | 65.6 | 37.0
Sum of all passes |  |  |  |  | 196.0 | 115.0
Chart: Screen opening (mm)
| 25 | 12.5 | 9.5299999999999994 | 6.3 | 4.75 | 2.38 | 1.19 | 0.84 | 0.1
2013.10.10.001.01 | 4.2926 | 16.2195 | 23.2344 | 26.0974 | 11.9434 | 13.366 | 3.4595 | 0.8819 | 0.50523
2013.10.10.001.01.A | 1.7499 | 42.6128 | 28.2029 | 16.289 | 6.8112 | 2.6252 | 1.4553 | 0.24299 | 0.010634 | 0
2013.10.10.001.01.A.A | 0 | 1.0114 | 12.9673 | 39.89 | 28.226 | 10.8794 | 5.9303 | 1.0957 | 0 | 0
2013.10.10.001.01.A.A.A | 0 | 0.012326 | 1.4523 | 26.9323 | 38.7004 | 19.1288 | 11.4474 | 2.3018 | 0.02462 | 0
1.6mm
Note: size shown to 1.6mm for comparison with hammermill

## Slide 16: Precision Feedstocks® Supply Chain Manufacturing and Cost Modeling
Capacity | Capital ($ millions) | 
odMg/day | Total | Equipment
100 | 3.8 | 2.1
400 | 15.5 | 9.5
1000 | 37.2 | 23.8

## Slide 17: Crumbler vs Hammermill Size Distribution and Energy
Chart: Screen opening (mm)
| 9.5299999999999994 | 4.75 | 3.1749999999999998 | 2 | 1.18 | 0.85 | 0.5 | 0.3 | 0.15 | 0.1
Crumbled | 0 | 0.012326 | 1.4523 | 26.9323 | 38.7004 | 19.1288 | 11.4474 | 2.3018 | 0.02462 | 0
Hammermilled | 0.060987 | 0.076219 | 0.64033 | 7.8094 | 39.1048 | 34.5401 | 16.0116 | 1.6345 | 0.091678 | 0.030522
Chart: MJ/odMG
| Crumbler | Crumbler | Hammermill | Hammermill | As recorded | Optimized | No Blower | With Blower
Specific | 115 | 115 | 690 | 690
Avg. Noload | 81 | 39 | 760 | 1660
Particle Size Distribution
Comminution Energy (55% MC)

## Slide 18: Crumbling Energy Cost from Chips
Comminution energy cost (Total Energy $/US Ton) for Optimized Crumbler® machine as a function of final size from poplar wood chips having an initial geometric mean particle size (Xgm) of 12 mm.
Chart: Final Particle Size (Xgm, mm)
| 12 | 5.39 | 2.63 | 1.97 | 1.23 | 0.98
Total E | 0.018905 | 0.36865 | 1.4746 | 2.1741 | 3.5504 | 4.5278
Specific E | 0.014179 | 0.27649 | 1.1059 | 1.6306 | 2.6628 | 3.3958

## Slide 19: Bioproducts Opportunities

## Slide 20: Relevance
Higher particle uniformity & flowability has positive downstream conversion benefits
Lower comminution energy costs reduce feedstock costs
Higher capital and maintenance costs than hammer-mills
Processing high-moisture biomass to small sizes reduces dryer capital and operating costs

## Slide 21: Thank You
Development was supported in-part by the Small Business Innovation Research program of the U.S. Department of Agriculture contract 2013-33610-20827
Development was supported by US Department of Energy SBIR contracts DE-SC0002291 and DE-SC-0010122.
Mike Perry
mperry@forestconcepts.com
Forest Concepts, LLC
3320 W. Valley Hwy. N., STE D110
Auburn, WA 98001
253.333.9663
www.forestconcepts.com
Jim Dooley
jdooley@forestconcepts.com
Notes: This project was supported in-part by the CSREES Small Business Innovation Research program of the U.S. Department of Agriculture, grant number # 2006-33610-17595.